## Slide 1: The Memory Hierarchy 15-213: Introduction to Computer Systems 11th Lecture, Oct. 6, 2015
Instructors:
Randal E. Bryant and David R. O’Hallaron

## Slide 2: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 3: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
RAM comes in two varieties:
  SRAM (Static RAM)
  DRAM (Dynamic RAM)

## Slide 4: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers

## Slide 5: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs. with partial (block-level) erase capability
    Wears out after about 100,000 erasings
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 6: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 7: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 8: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%rax
I/O bridge
Load operation: movq A, %rax

## Slide 9: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %rax.
x
ALU
Register file
Bus interface
x
Main memory
0
A
%rax
I/O bridge
Load operation: movq A, %rax

## Slide 10: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 11: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 12: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
Register file
Bus interface
y
main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 13: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 14: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 15: Disk Geometry (Muliple-Platter View)
Aligned tracks form a cylinder.
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Cylinder k
Spindle
Platter 0
Platter 1
Platter 2

## Slide 16: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 109 Bytes.
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.

## Slide 17: Recording zones
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track, outer zones have more sectors/track than inner zones.
  So we use average number of sectors/track when computing capacity.
Spindle
…

## Slide 18: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 19: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 20: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle

## Slide 21: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 22: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 23: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 24: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 25: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 26: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 27: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 28: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 29: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 30: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 31: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical Tavg rotation = 7200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 32: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 33: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.
Allows controller to set aside spare cylinders for each zone.
  Accounts for the difference in “formatted capacity” and “maximum capacity”.

## Slide 34: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 35: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 36: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 37: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 38: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after about 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 39: SSD Performance Characteristics
Sequential access faster than random access
  Common theme in the memory hierarchy
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms)
  Modifying a block page requires all other pages to be copied to new block
  In earlier SSDs, the read/write gap was much larger.
Sequential read tput 550 MB/s Sequential write tput 470 MB/s
Random read tput 365 MB/s Random write tput 303 MB/s
Avg seq read time 50 us Avg seq write time 60 us
Source: Intel SSD 730 product specification.

## Slide 40: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Intel SSD 730 guarantees 128 petabyte (128 x 1015 bytes) of writes before they wear out
  In 2015, about 30 times more expensive per byte
Applications
  MP3 players, smart phones, laptops
  Beginning to appear in desktops and servers

## Slide 41: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk

## Slide 42: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 43: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 44: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 45: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 46: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 47: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 48: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 49: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 50: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 51: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 52: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 53: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 54: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 55: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 56: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 57: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 58: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 59: Supplemental slides

## Slide 60: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 61: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 62: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 63: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit word main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit word
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 64: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports only DDR3 SDRAM

## Slide 65: Storage Trends
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 880 100 30 1 0.1 0.06 0.02 44,000
access (ns) 200 100 70 60 50 40 20 10
typical size (MB) 0.256 4 16 64 2,000 8,000 16.000 62,500
DRAM
SRAM
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/GB 100,000 8,000 300 10 5 0.3 0.03 3,333,333
access (ms) 75 28 10 8 5 3 3 25
typical size (GB) 0.01 0.16 1 20 160 1,500 3,000 300,000
Disk
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 2,900 320 256 100 75 60 320 116
access (ns) 150 35 15 3 2 1.5 200 115

## Slide 66: CPU Clock Rates
1985 1990 1995 2003 2005 2010 2015 2015:1985
CPU 80286 80386 Pentium P-4 Core 2 Core i7(n) Core i7(h)
Clock
rate (MHz) 6 20 150 3,300 2,000 2,500 3,000 500
Cycle
time (ns) 166 50 6 0.30 0.50 0.4 0.33 500
Cores 1 1 1 1 2 4 4 4
Effective
cycle 166 50 6 0.30 0.25 0.10 0.08 2,075
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”
(n) Nehalem processor
(h) Haswell processor